## Slide 1: CSTE-2105 Digital logic design

## Slide 3: Outline
Digital and analog systems
Number systems and codes

## Slide 4: Numerical representations of Quantities
It is important when dealing with various quantities that we be able to represent their values efficiently and accurately.
Basic two ways of representing the numerical value of quantities: analog and digital

## Slide 5: Numerical representations of Quantities
Analog: Continuous
Digital: Discrete (step by step)
Example: Thermometer. Temperature with a mercury is analog quantity. Nearest line selection over a continuous range is digital

## Slide 6: Numerical representations of Quantities Example:
Ten position switch (D)
Current flowing from an electrical outlet (A)
Temperature of a room (A)
Sand grains on the beach (D)
Automobile fuel gauge (A/D)

## Slide 7: Digital and analog Details
Book reference: Digital Systems by Ronald J. Tocci

## Slide 8: Digital and analog Details (Home work)
Questions:
Advantages of digital techniques over analog.
Limitations of digital technique.
Conversion steps from analog-digital-analog.

## Slide 9: Number system
Decimal number system is the most common number system. Other popular number systems include binary number system, octal number system, hexadecimal number system, etc.

## Slide 10: Decimal number system
Decimal number system is a base 10 number system having 10 digits from 0 to 9. This means that any numerical quantity can be represented using these 10 digits. Decimal number system is also a positional value system. This means that the value of digits will depend on its position.
Say we have three numbers – 734, 971 and 207. The value of 7 in all three numbers is different−
In 734, value of 7 is 7 hundreds or 700 or 7 × 100 or 7 × 102
In 971, value of 7 is 7 tens or 70 or 7 × 10 or 7 × 101
In 207, value 0f 7 is 7 units or 7 or 7 × 1 or 7 × 100

## Slide 11: Decimal number system
The weightage of each position can be represented as follows −

## Slide 12: Decimal number system
In digital systems, instructions are given through electric signals; variation is done by varying the voltage of the signal. Having 10 different voltages to implement decimal number system in digital equipment is difficult. So, many number systems that are easier to implement digitally have been developed.

## Slide 13: Binary number system
The easiest way to vary instructions through electric signals is two-state system – on and off. On is represented as 1 and off as 0, though 0 is not actually no signal but signal at a lower voltage. The number system having just these two digits : 0 and 1 is called binary number system.
Each binary digit is also called a bit. Binary number system is also positional value system, where each digit has a value expressed in powers of 2.

## Slide 14: Binary number system
In any binary number, the rightmost digit is called least significant bit (LSB) and leftmost digit is called most significant bit (MSB).

## Slide 15: Binary number system
…and decimal equivalent of this number is sum of product of each digit with its positional value.
110102 = 1×24 + 1×23 + 0×22 + 1×21 + 0×20
= 16 + 8 + 0 + 2 + 0
= 2610
Computer memory is measured in terms of how many bits it can store. Here is a chart for memory capacity conversion.
1 byte (B) = 8 bits
1 Kilobytes (KB) = 1024 bytes
1 Megabyte (MB) = 1024 KB
1 Gigabyte (GB) = 1024 MB
1 Terabyte (TB) = 1024 GB
1 Exabyte (EB) = 1024 TB
1 Zettabyte = 1024 EB
1 Yottabyte (YB) = 1024 ZB

## Slide 16: Octal number system
Octal number system has eight digits – 0, 1, 2, 3, 4, 5, 6 and 7. Octal number system is also a positional value system with where each digit has its value expressed in powers of 8, as shown here −Decimal equivalent of any octal number is sum of product of each digit with its positional value.
7268 = 7×82 + 2×81 + 6×80
= 448 + 16 + 6
= 47010

## Slide 17: Hexadecimal number system
Hexadecimal number system has 16 symbols – 0 to 9 and A to F where A is equal to 10, B is equal to 11 and so on till F. Hexadecimal number system is also a positional value system with where each digit has its value expressed in powers of 16
27FA16 = 2×163 + 7×162 + 15×161 + 10×160
= 8192 + 1792 + 240 +10
= 1023410

## Slide 18: Relationship among number systems
HEXADECIMAL | DECIMAL | OCTAL | BINARY
0 | 0 | 0 | 0000
1 | 1 | 1 | 0001
2 | 2 | 2 | 0010
3 | 3 | 3 | 0011
4 | 4 | 4 | 0100
5 | 5 | 5 | 0101
6 | 6 | 6 | 0110
7 | 7 | 7 | 0111
8 | 8 | 10 | 1000
9 | 9 | 11 | 1001
A | 10 | 12 | 1010
B | 11 | 13 | 1011
C | 12 | 14 | 1100
D | 13 | 15 | 1101
E | 14 | 16 | 1110
F | 15 | 17 | 1111
The following table depicts the relationship between decimal, binary, octal and hexadecimal number systems.