## Slide 1: Clock pulse generator

## Slide 2: Astable Multivibrator Mode of 555 Timer IC
Astable multivibrator is also called as Free Running Multivibrator. It has no stable states and continuously switches between the two states without application of any external trigger. The IC 555 can be made to work as an astable multivibrator with the addition of three external components: two resistors (RA and RB) and a capacitor (C).

## Slide 3: Astable Multivibrator Mode of 555 Timer IC

## Slide 4: Astable Multivibrator Mode of 555 Timer IC

## Slide 5: Astable Multivibrator Mode of 555 Timer IC
Initially, on power-up, the flip-flop is RESET (and hence the output of the timer is low). As a result, the discharge transistor is driven to saturation (as it is connected to ).The capacitor C of the timing circuit is connected at Pin 7 of the IC 555 and will discharge through the transistor. The output of the timer at this point is low. The voltage across the capacitor is nothing but the trigger voltage. So, while discharging, if the capacitor voltage becomes less than 1/3 VCC, which is the reference voltage to trigger comparator (comparator 2), the output of the comparator 2 will become high. This will SET the flip-flop and hence the output of the timer at pin 3 goes to HIGH.

## Slide 6: Astable Multivibrator Mode of 555 Timer IC
This high output will turn OFF the transistor. As a result, the capacitor C starts charging through the resistors RA and RB. Now, the capacitor voltage is same as the threshold voltage (as pin 6 is connected to the capacitor resistor junction). While charging, the capacitor voltage increases exponentially towards VCC and the moment it crosses 2/3 VCC, which is the reference voltage to threshold comparator (comparator 1), its output becomes high.
As a result, the flip-flop is RESET. The output of the timer falls to LOW. This low output will once again turn on the transistor which provides a discharge path to the capacitor. Hence the capacitor C will discharge through the resistor RB. And hence the cycle continues.

## Slide 7: Astable Multivibrator Mode of 555 Timer IC
Thus, when the capacitor is charging, the voltage across the capacitor rises exponentially and the output voltage at pin 3 is high. Similarly, when the capacitor is discharging, the voltage across the capacitor falls exponentially and the output voltage at pin 3 is low. The shape of the output waveform is a train of rectangular pulses.

## Slide 8: Astable Multivibrator Mode of 555 Timer IC

## Slide 9: Astable Multivibrator Mode of 555 Timer IC

## Slide 10: Example:
Calculate the frequency and the duty cycle of the 555 astable multivibrator output for C= 0.001 F, RA= 2.2 k k

## Slide 11: Digital arithmetic: operation and circuits

## Slide 12: Binary addition

## Slide 13: Binary addition
a. Decimal addition (sum, carry) b. General steps of binary addition.

## Slide 14: Examples

## Slide 15: Representing signed number
In digital computers, binary numbers are represented by a set of binary storage devices (FFs). Each device represents one bit. Example: A six bit FF register can store binary numbers ranging from 000000-111111 (0-63 decimal). This represents the magnitude of the number.
Most digital computers and calculators handle negative as well as positive numbers, some means is required for representing the sign of the number (+ or -). This is usually done by adding to the number another bit called the sign bit. In general, 0 represents the positive number and 1 represents the negative number.

## Slide 16: Representing signed number
Example: For a six bit number with sign number, the MSB represents sign bit and the rest bits represents the magnitude of the number.

## Slide 17: 1’s/2’s complement

## Slide 18: 1’s complement form
The 1’s complement of a binary number is obtained by changing each 0 to a 1 and each 1 to a 0. In other words, change each bit in the number to it’s complement.

## Slide 19: 2’s complement form
The 2’s complement of a binary number is formed by taking the 1’s complement of the number and adding 1 to the LSB position.

## Slide 20: Representing signed number using 2’s complement
Convert +4510 in its true binary form.
If the number is negative -45, then how can you represent this?
Note: 2’s complement represents signed numbers. It allows us to perform the operation of subtraction by accurately performing addition. This is significant because it means that a digital computer can use the same circuitry both to add and to subtract, thereby analyzing a saving in hardware.

## Slide 21: Representing signed number using 2’s complement

## Slide 22: Example (homework)
+13
-9
+3
-2
-8

## Slide 23: Sign extension
The size of the register (FFs no.) determines the number of binary digits. Registers size is the even multiple of 4 bits. The storage registers will be made up of 4, 8, 12, 16, 32 or 64.
For example, if we need to store a positive 5 bit number in a 8 bit register, it make sense to simply add leading zeros.

## Slide 24: Sign extension
+9 = 000 0 1001(in 8 bit register)
-9 = 1 0111 (5 bit representation)
-9 = ?? (in 8 bit register)

## Slide 25: Negation
We negate a signed binary number by 2’s complementing it.

## Slide 26: Example:
Each of the following numbers is a five bit signed binary number in the 2’s 2’s complement system. Determine the decimal value in each case.
1 1010
1 0001

## Slide 27: Example:

## Slide 28: Special case in 2’s complement:
Whenever a signed number has a 1 in the sign bit and all 0s for the magnitude bits , its decimal equivalent is -, where N is the number of bits in the magnitude. For example-
The complete range of values that can be represented in the 2’s
Complement system having N magnitude bits is

## Slide 29: Special case in 2’s complement

## Slide 30: Addition in 2’s complement

## Slide 31: Addition in 2’s complement
1. Two positive numbers 2. Positive number and smaller negative number 3. Positive number and larger negative number 4. two negative numbers 5. equal and opposite number

## Slide 32: Subtraction in 2’s complement

## Slide 33: Subtraction in 2’s complement
Procedure: 1. Negate the subtrahend 2. Add this to the minuend

## Slide 34: Subtraction in 2’s complement
Procedure: 1. Negate the subtrahend 2. Add this to the minuend

## Slide 35: Arithmetic overflow
Overflow into the sign bit position. This overflow condition can occur when two positive or two negative numbers are being added and it always produces an incorrect result. For 2’s complement subtraction overflow can occur when minuend and subtrahend have different sign. Computer will have special circuit to detect any overflow condition.

## Slide 36: Bcd addition

## Slide 37: BCD Addition
1. Sum equals to 9 or less

## Slide 38: BCD Addition (correction)
2. sum greater than 9
3. Correction

## Slide 39: BCD Addition (correction)
2. sum greater than 9
3. Correction