## Slide 1: Peripheral Interface Device (8255 modes and examples)
Dr A Sahu
Dept of Computer Science & Engineering
IIT Guwahati

## Slide 2: Hierarchy of I/O Control Devices
8155
I/O + Timer
8255
I/O
8253/54
Timer
2 Port (A,B),
No Bidirectional
HS mode (C)
4 mode timer
2 Port (A,B)
A is Bidirectional
HS mode (C)
Extra controls
6 mode timer
8259
Interrupt controller
8237
DMA controller
8251
Serial I/O USART controller

## Slide 3: Outline
8255 Architecture and its block diagram
8255 Ports and mode of operations
BSR Mode
Mode 0
  Interfacing A/D Converter using Handshake mode using 8255
Mode 1
  Interfacing DIP keyboard using Handshake mode using 8255
Mode 2
  Interfacing keyboard (with bounce) using Handshake mode using 8255
Introduction to interrupt controller (8259A)

## Slide 4: Block Diagram of 8255
Group A
Control
Group B
Control
Read
Write
Control Logic
Data
Bus
Buffer
Gr A
Port A
(8)
Gr A
Port C
(H 4)
Gr B
Port C
(L 4)
Gr B
Port B
(8)
I/O
PA7-PA0
I/O
PC7-PC4
I/O
PC3-PC0
I/O
PB7-PB0
8 bit Internal Data Bus
Bi directional
Data Bus
D7-D0
RDb
WRb
A1
A0
RESET
CSb
CSb | A1 | A0 | Sel
0 | 0 | 0 | Port A
0 | 0 | 1 | Port B
0 | 1 | 0 | Port C
0 | 1 | 1 | CRW

## Slide 5: Ports & Modes in 8255
Port C
D7 D6 D5 D4 D3 D2 D1 D
BSR Mode
Bit Set/Reset
8255
Port B
CU
CL
Port A
I/O Mode
Mode 0
Simple I/O for Ports
A, B & C
Mode 1
HS mode
for Ports
A and/or B
Port C bits are used for
HS
Mode 2
Bidirectional
Data mode for Port
A
B can in mode 0/1
Port C bits are used for HS
BSR Mode
Bit Set/Reset
For Port C
No Effect on
I/O Mode
0/1

## Slide 6: Ports & Modes in 8255 : Control register
D7 D6 D5 D4 D3 D2 D1 D0
7 6 5 4 3 2 1 0
Port A – 1 Input 0 output
Mode select: 00 mode 0;
01 mode 1; 1x mode 2
1 – mode select
0 – bit set/reset
Port C(U) – 1 Input 0 output
Mode select: 0 mode 0; 1 mode 1
Port B – 1 Input 0 output
Port C(L) – 1 Input 0 output
Group A
Group B

## Slide 7: I/O port Addressing
8255
CSb
A1
A0
RDb
WRb
A7
A6
A5
A4
A3
A2
A1
A0
IORb
IOWb
Reset
Reset
Port A=80H
Port C=82H
Port B=81H
CSb | A1 A0 | HEX Address | Port
A7 A6 A5 A4 A3 A2 1 0 0 0 0 0 | A1 A0 0 0 | = 80H | A
 | 0 1 | =81H | B
 | 0 | =82H | C
 | 1 | =83H | Control Register
CRW
83H

## Slide 8: Ports
Control register controls the overall operation of 8255
All three ports A, B and C are grouped into two
Group B
Group A
Port A
Upper C
Port B
Lower C

## Slide 9: Operation modes
8255 has three modes:
- Mode 0: basic input-output
- Mode 1: Strobbed input-output
- Mode 2: Strobbed bi-directinal bus I/O
In mode 0
- Two 8-bit ports and two 4-bit ports
- Any port can be input or output
- Outputs are latched, inputs are not latched

## Slide 10: Operation modes
In mode 1:
-Three ports are divided into two groups
-Each group contains one 8-bit port and one 4-bit control/data port
- 8-bit port can be either input or output and both latched
- 4-bit port used for control and status of 8-bit data port
In mode 2
- Only port A is used
- Port A becomes an 8-bit bidiectional bus
- Port C acts as control port (only pins PC3-PC7 are used)

## Slide 11: BSR (Bit Set or Reset Mode)
Set/Reset bit of Port C
Heavily used for HS and Interrupt mode
BSR Control word
BSR Control word
  To set PC7= 0 000 111 1 (0FH)
  To reset PC7= 0 000 111 0 (0EH)
  To set PC3 = 0 000 011 1 (07H)
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 BSR Mode | Not used, So (000) |  |  | Bit Select |  |  | S/R (1/0)

## Slide 12: BSR Mode example
BSR Control word
  To set PC7= 0 000 111 1 (0FH)
  To reset PC7= 0 000 111 0 (0EH)
  To set PC3 = 0 000 011 1 (07H)
  Generate Activation pulse of Delay D on PC7&PC3
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 BSR Mode | Not used, So (000) |  |  | Bit Select |  |  | S/R (1/0)
  MVI A,0FH ; Load ACC to set PC7
  OUT 83H ; set PC7=1
  MVI A,07H ; Load ACC to set PC3
  OUT 83H ; set PC3=1
  CALL DELAYD;
  MVI A,06H ; Load ACC to Reset PC3
  OUT 83H ; set PC3=1
  MVI A,0EH ; Load ACC to Reset PC7
  OUT 83H ; set PC7=1

## Slide 13: 8255: Mode 0
Simple I/O for port A,B,C
Output are latched
Input are not latched
Port don’t have HS or interrupt capability

## Slide 14: 8255: Mode 0, Example 1
Configure
  Port A and port CU as out port
  Port B and port CL as in port
Interface to Read from I/P DIPs and Display at O/P LEDs
Control word
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
I/O function | Port A in Mode 0 |  | Port A as O/P | Port CU As O/P | Port B in Mode 0 | Port B As I/P | Port CL As I/P
83H

## Slide 15: Interface Circuit
8255
CSb
A1
A0
RDb
WRb
A7
A6
A5
A4
A3
A2
A1
A0
IORb
IOWb
Reset
Reset
Buffer
Buffer
+5V
+5V
PA7
PA0
PC7
PC4
PC3
PC0
PB7
PB0
80H
82H
82H
81H
CRW
83H

## Slide 16: Interface Program
MVI A,83H ; Load acc with Control word
OUT 83H ; Load control register with 83 at port address 83
IN 81H ; Read DIP from port B
OUT 80H ; Write to LEDs
IN 82H ; Read DIP from port C
ANI 0FH ; Mask upper part of
port C are not i/p
RLC RLC RLC RLC; Rotate 4 time
OUT 82H ; Display data at port CU
HLT

## Slide 17: 8255: Mode 0, Example 2
Air Conditioning Room (Temperature Control)
  Heater and Cooler
  Temperature Sensor
  A/D converter
  Driver Switch to drive Heater/Cooler
Design an A/C controller using 8255 and 8085 based interfacing circuit
Read temperature and control the temperature between 20-30 degree Celciuous

## Slide 18: 8255: Mode 0, Example 2
Air Conditioning Room (Temperature Control)
  Heater and Cooler
  Temperature Sensor
  A/D converter
  Driver Switch to drive Heater/Cooler
Design an A/C controller using 8255 and 8085 based interfacing circuit
Read temperature and control the temperature between 20-30 degree Celsius
Use port A in mode 0 and Port C in BSR mode

## Slide 19: Interface Circuit
8255
CSb
A1
A0
RDb
WRb
A7
A6
A5
A4
A3
A2
A1
A0
IORb
IOWb
Reset
Reset
PA7
PA0
PC0
PC4
PC7
PC5
PC6
CRW
83H
data
ADC
INTRb
WRb
RDb
LM135 Temp Sensor
+5V
Relay
Relay
Cooler
Heater
+ -
230V

## Slide 20: Interface control
Control word
  Port A as I/P from ADC
  Port CL : as I/P PC0 is used for end of conversion
  Port CU : as O/P PC4 -> Start con. PC7 ->assert RDb signal
BSR Control word
  0 (mode) 000 (don’t care) 000 (0/1=set/reset)
  Set PC7 high = 0 000 111 1 = 0FH (Send RDb to ADC)
  Set PC4 low = 0 000 100 0 = 08F (send Start Conv WRb)
  Set PC5 high = 0 000 101 1 = 0BF (Fan On)
  Set PC5 low = 0 000 101 0 = 0AF (Fan Off)
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1
I/O function | Port A in Mode 0 |  | Port A as I/P | Port CU As O/P | Port B Is Not used |  | Port CL As I/P
91H

## Slide 21: Interface Program to do Temp. Control
MVI A, 91H ; mode 0 control word
OUT 83H ; Set A& CL as I/P & CU as
O/P
MVI A,0FH ;Set PC7 High
OUT 83H ; Disable RDb
MVI A,08H ; Set PC4 WRb low
OUT 83H ; Start conversion
MVI A, 09H ; Set PC4 WRb high
OUT 83H ; Ser WRb high
RD: IN 82H ; Read Port C to Chck PC0
RAR ; Place PC0 in Carry Flag
JC RD ;if PC0=1, read Again
MVI A,0EH ; Set PC7 RDb low
OUT 83H ; Assert RDb signal
IN 80H ; Read A/D conv. Port A
MOV B,A ; get temp in B
MVI A 0FH; ; Set PC7 (RDb) high
OUT 83 ; Disable RDb
MOV A,B;
CPI 30D;
CNC COOLEROFF; PC5 off 0AH
CC COOLERON; PC5 on 0BH
CPI 10D;
MOV A,B;
CNC HEATERON; PC6on: 0CH
CC HEATEROFF; PC6off: 0DH
RET
COOLEROFF:
MVI A, 0AH ; Reset PC5 to turn off Cooler
OUT 83H
RET

## Slide 22: 8255: Mode 1
Two port A & V function 8 bit I/O
  Configured either Input or output port
Each port each 3 lines of port C as HS signal
  Remaining two lines can be used as simple I/O
Input and output are latched
Interrupt logic is supported
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 0 | 1 | 0 | 0/1 | 1 | 1 | X=0
I/O function | Port A in Mode 1 |  | Port A as O/P | Port CU As O/P | Port B in Mode 1 | Port B As I/P | Port CL As I/P
AEH
PC6, PC7 in
In/Out mode

## Slide 23: 8255: Mode 1: Input Control signal
STBb: Strobe generated by Peripheral
IBF: Input buffer full
  Acknowledge by 8255 to I/O that I/O latched received
  Reset when MPU read the data
INTR: output signal to MPU and it generate when STBb=1, IBF=1 and INTE=1
INTE: Enable or disable Interrupt
  INTEA is through PC4, INTEB is through PC2
Status word
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
OBFbA | INTEA | 1/0 | 1/0 | INTRA | INTEB | OBFbB | INTRB
Mask with 02H

## Slide 24: 8255: Mode 1, Example
Designing for interfacing
  Keyboard with interrupt I/O in port A
  Output port for a printer using status check I/O
Control word
To generate interrupt INTEA PC4 to set in BSR mode
  0 (mode) 000 (don’t care) 000 (0/1=set/reset)
  Set PC4 High = 0 000 100 1 = 09F (send INTR to MPU RST 6.5)
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
I/O function | Port A in Mode 1 |  | Port A as I/P | PC6,7 as X | Port B in Mode 1 | Port B As O/P | Don’t care
B4H

## Slide 25: Interface Circuit
8255
CSb
A1
A0
RDb
WRb
A1
A0
IORb
IOWb
Reset
PA7
PA0
PC4
PC5
PC3
PC1
PC2
PB7
PB0
CRW
83H
data
KBD
Printer
STBb
IBF
INTRA
OBFb to PTR
ACKb
80A
81H
To
RST 6.5
A7
A6
A5
A4
A3
A2

## Slide 26: Interface Program
Initialization Program
MVI A, B4H ; initialize port A as IP and B
as O/P
OUT 83H
MVI A,09H ; Set INTEA , that is PC4
EI ;Enable interrupt
CALL PRINT ; Continue other Task
ISR at 0034 at RST6.5 vector location
0034: JMP READPORTA
READ PORTA:
DI
IN 80H
MOV M, A
INX H
EI
RET
PRINT: LXI H MEM
MVI B COUNT
MOV A,M
MOV C,A
STATUS: IN 82H ; from port C for
Status OBFb
ANI 02H
JNZ STATUS
MOV A,C
OUT 81H; Send to port B
printer
INX H
DCR B
JNZ NEXT
RET

## Slide 27: 8255: Mode 2: Bi-directional Data transfer
Bi-directional
  Data transfer between two MPU
  Data transfer between MPU and Controller
Port A can be bi-directional, Port B in either 0 or 1 mode
Port A use 5 signals from port C as Handshake signal for data transfer

## Slide 28: Bi-directional Data transfer between two MPU
One is Master other is Slave
Use 8255 as Interfacing device
Master
MPU
Slave
MPU
8255
OBFb
ACKb
IBF
STBb
Decode
Logic
CSb
RDb
WRb
PC7
PC6
PC5
PC4
PC3

## Slide 29: Data Transfer From Mater to Slave
Master read the status of OBF to verify whether the previous byte has read by Slave
Mater write date in port A and 8255 inform to Slave by OBFb low
Slave check OBF for data availability
Slave read the data from port A and ACK low to 8255

## Slide 30: Data Transfer From Slave to master
Slave check the HS signal IBF to find out whether port A is available or not
Slave Write a data in port A and inform 8255 by enabling STBb low
8255 causes a IBF to go high and MPU get the signal the data byte to read
Master read the data from port A and make IBF low

## Slide 31: Interface Circuit
Slave
MPU
8255
CSb
A1
A0
RDb
WRb
A1
A0
IORb
IOWb
Reset
PA7
PA0
PC7
PC5
PC6
PC4
CRW
83H
data
ACKb
A7
A6
A5
A4
A3
A2
data
Latch
TriState
STBb
IORb
Master
MPU
IORb
IOWb
3to8 Decoder
07
05
00
D7
D0
A7
A6
A5
A2
A1
A0
EN
80H=A
81H=B
82H=C
83H=CRW
85H = A
87H = C

## Slide 32: Control word Mode 2
Control word
Status word:
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | 1 | X | X | X | 1/0 | 1/0 | 1/0
I/O function | Port A in Mode 1 |  | Port A as Bi |  | Port B in Mode 1/0 | Port B As 1/0 | Port C
Port C bit 2,1,0 mode 0/1
C0H
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
OBFA | INTE1 | IBFA | INTE2 | INTRA | X | X | X
RAL instruction to get the Status

## Slide 33: Interface program: Master & Slaves
Master:
LXI H, MemptrM
MVI B, Byte2Trasfer
MVI A, CTRL; Control word for
Mode 2
OUT 83H; Write Control word
OBFLO:
IN 82H ; Read port C
RAL ; place OBF in CY
JNC OBFLO;
OUT 80H ; place on Port A
INX H
DCR B
JNZ OBFLO
HLT
SLAVE:
LXI H, MemptrS
MVI B, Byte2Trasfer
OBFHI:
IN 87H ; Read port C
RAL ; place OBF in CY
JC OBFHI;
IN 85H ; Read from Port A
MOV M, A
INX H
DCR B
JNZ OBFHI
HLT

## Slide 34: Introduction to Interrupt controller 8259A
Acts as a multiplexer, combining multiple interrupt input sources into a single interrupt output to interrupt a single device.
Original PC introduced in 1981
Eight interrupt input request lines
  IRQ0 - IRQ7,
  An interrupt request output line named INTR
  Interrupt acknowledgment line named INTA
  D0 through D7 for communicating the interrupt level or vector offset.
There are three registers
  Interrupt Mask Register (IMR)
  Interrupt Request Register (IRR)
  In-Service Register (ISR)

## Slide 35: Reference
R S Gaonkar, “Microprocessor Architecture”, Chapter 15

## Slide 36: Thanks