## Slide 1: Session 2020-21 CSTE-3101 Communication Engineering

## Slide 2: Week: 4-8

## Slide 3: Book Reference
Modern digital and analog communication: B. P Lathi
Communication systems by Simon S. Haykin
Communication systems: Analog and Digital by Sanjay Sharma
Data Communications and Networking by Behrouz A. Forouzan, McGraw-Hill.

## Slide 4
Overview of Communication System

## Slide 9
Hertzian antenna

## Slide 15
m(t)=Am cos 2pifmt

## Slide 19
Synchronous detector/ coherent detector

## Slide 25: Analog and Digital Signal

## Slide 26: Periodic Analog Signal
Example:
Sine Wave
Period: T=1/f ; unit= second
Frequency: f=1/T; unit=hertz

## Slide 27: Periodic Analog Signal
Phase/ Phase shift: It describes the position of the waveform relative to time 0

## Slide 28: Periodic Analog Signal
Wavelength:
It is another characteristic of a signal traveling through a transmission medium. Wavelength binds the period or the frequency of a simple sine wave to the propagation speed of the medium.
Unit: µm, nm, m, km etc.

## Slide 29: Time and Frequency Domain
A sine wave is defined by its amplitude, frequency and phase.
To show a sine wave by using what is called a time-domain plot (amplitude (y-axis) vs time (x-axis) plot).
To show the relationship between amplitude and frequency by using what is called a frequency-domain plot. A frequency-domain plot is concerned with only the peak value and the frequency. Changes of amplitude during one period are not shown.

## Slide 30: Time and Frequency Domain

## Slide 31: Time and Frequency Domain (composite signal)

## Slide 32: Bandwidth
A single frequency sine wave is not useful in data communication. We need to send a composite signal, a signal made of many simple sine waves. The range of frequencies contained in a composite signal is its bandwidth. The bandwidth of a composite signal is the difference between the highest and the lowest frequencies contained in that signal. If a composite signal contains frequencies between 1000-5000, its bandwidth is (5000-1000)=4000.
Unit=hertz

## Slide 33: Bandwidth