## Slide 1: Number system and codes

## Slide 2: Decimal Number System
103 | 102 | 101 | 100 | . | 10-1 | 10-2 | 10-3
The weightage of each position for integer number:
For fractional number:
The decimal point is used to separate the integer and fractional parts of the number.

## Slide 3: Example (sum of product method)
27.3510
= 2×101 + 7×100 + 3×0.1 + 5×0.01

## Slide 4: Example Binary to decimal conversion
1011.1012
= 1×23 + 0×22+ 1×21 + 1×20 + 1×2-1 + 0×2-2 +1×2-3
= 8+0+2+1+0.5+0+0.125
= 11.62510

## Slide 5: Example Octal to decimal conversion
24.688
= 2×81 + 4×80 + 6×8-1 +8×8-2
= 16+4+0.75+0.125
= 20.87510

## Slide 6: Example Hex to decimal conversion
1F.01B16
= 1×161 + 15×160 + 0×16-1 +1×16-2 + 11×16-3
= 31.006591810

## Slide 7: Reverse calculation

## Slide 8: Repeated division method

## Slide 9: decimal to binary conversion Repeated division method

## Slide 10: example decimal to binary conversion Repeated division method
Convert 2510 to binary number.
2510 = 110012

## Slide 11: example decimal to Octal conversion Repeated division method
Convert 26610 to octal number.
26610 = 4128

## Slide 12: example decimal to Hex conversion Repeated division method
Convert 42310 to octal number.
42310 = 1A716

## Slide 13: Mixed conversion

## Slide 14: example octal to binary conversion
Convert 4728 to binary number.
4728 = 1001110102
And
Convert 1001110102 to octal number.
1001110102= 4728
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
000 | 001 | 010 | 011 | 100 | 101 | 110 | 111

## Slide 15: example Hex to binary conversion
Convert 9F216 to binary number.
9F216 = 1001111100102
And
Convert 1001111100102 to hex number.
1001111100102= 9F216

## Slide 16: CODE

## Slide 17: CODE
When number, letters or words are represented by a special group of symbols , we say they are being encoded and the group of symbols is called a code. Example: Morse code

## Slide 18: BCD CODE
Each digit of decimal number is represented by its binary equivalent- called binary coded decimal code.
87410
= 1000 0111 0100BCD
BCD code doesn’t use A-F numbers.

## Slide 19: BCD vs binary
13710
= 100010012
= 0001 0011 0111BCD

## Slide 20: GRAY code
Only one bit ever changes between two successive numbers in the sequence.

## Slide 21: Binary-gray conversion
B2 | B1 | B0 | G2 | G1 | G0
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0

## Slide 22: GRAY-binary conversion
G2 | G1 | G0 | B2 | B1 | B0
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 1 | 1

## Slide 23: GRAY code

## Slide 24: At a glance